## Slide 1: Production and test of Si sensors for W-Si sandwich calorimeter
M.G.Song, M.W.Kim, J.H.Kang, Y.Kwon
( Yonsei Univ. ALICE Group)
together with PHENIX FOCAL efforts

## Slide 2: Contents
Introduction to W-Si sandwich calorimeter
Sensor production
  Design
  Fabrication
  Packaging
  Signal conditioning
Sensor test
  Cosmic test
  Beam test
Summary

## Slide 3: W-Si sandwich calorimeter, Basics
EM Shower in a typical prototype
20cm,  20X0,  1λ
15mm, RM

## Slide 4: W-Si sandwich calorimeter, Basics
EM Shower in a typical prototype

## Slide 5: Detector schematics

## Slide 6: W-Si sandwich calorimeter, Basics
Ideal for EM signal (, e, 0) under forward high multiplicity
  Compact EM shower inside calorimeter (W)
  3D tracking under large background possible though Si layers (Si)
  Easy adjustment of the detector granule (Si)
  Good energy resolution (W-Si)
  Expensive (Si), but we(Korea) can do well.

## Slide 7: Sensor production
  Sensor production
  6.2 cm x 6.2 cm n type wafer substrate and p type pattern
  4 x 4 (1.5cm each) pad : 16 channel per sensor

## Slide 8: Fabrication
Mask production
  Optical
  Electron lithography
ETRI Production
  Lithography
  Developing
  Implantation
  Etching

## Slide 9: Packaging
Micro module production
  Ceramic spacer
  INTC(Inter connect) board
  Silicon Sensor
  Cu foil
  epoxy plate

## Slide 10: Components for micro-module
Ceramic spacer
  Protection from warping and heat
INTC(Inter connect) board
  Electrical connection to sensor
Silicon Sensor
Cu foil
  Connection of sensor back plane to ground
Epoxy plate
  Electrical and physical protection
Notes: These are components for micro-module.
This one is a silicon sensor which is the most important part of a micro-module.
On the front of sensor, INTC board is attached.
In this board, there are some RC components to connect to sensor electrically.
Below the sensor, Cu foil is used to connect sensor back plane with ground.
Cu foil INTC board are used for electrical connection.
Ceramic spacer and Epoxy plate are used for electrical and physical protection.
Especically, ceramic spacer locates between INCT board and carrier board, so it protect both boards from electrical connection and heat.

## Slide 11: Signal conditioning

## Slide 12: Cosmic muon test
Most electrons passing a sensor layer are MIPs, which deposit minimum ionization energy as like cosmic muon.
Cosmic test requires a setup of test electronics made up of silicon sensor, preamp hybrid card, test board, and bridge board.

## Slide 13: Cosmic muon test

## Slide 14: Cosmic muon test

## Slide 16: Beam test at CERN
Beam test had been taken 09.06.22~29 at PS and SPS
4 Sensor were used for each layer, and a super module had 7 W-Si layers.

## Slide 17: Beam test setup

## Slide 20: Summary
W-Si calorimeter can effectively measure EM signal under large multiplicity
Si sensor plays a key roll in the function
We are conducting production & test of the Si sensors and see a good prospect